## Slide 1: LJ - X8400 Laser Scanner
Measurement Application
Group Members
Muhammad Zeeshan Yousaf (Slide 1-10)
Kasmin Talukdar (Slide 11-15)
Ashwini Joshi (Slide 16-20)
Utkarsh Mishra (Slide 17-26)
Muhammad Hasan Khan (Slide 27-36)
Amritha Anitha Vasanthan (Slide 37-45)
Muhammad Zeeshan Yousaf

## Slide 2: Contents
Project Requirements
Mount for Sensor
Structure of Layout
Details of Sensor and Controller
Data Flow of App
Details of Back End
Details of Front End
Live Data Page
2D Capture Data Page
2D Compare Data Page
3D Data Page
Muhammad Zeeshan Yousaf

## Slide 3: Project Requirements
Development of Web based or native app.
Acquisition of live Data from the sensor.
Measurement of 2d data
Comparison of 2d data
3D construction of object using scans from several time stamps
Creating a mount for sensor to mount sensor on a table or a robot
Muhammad Zeeshan Yousaf

## Slide 4: Mount For Sensor
Muhammad Zeeshan Yousaf

## Slide 5: Structure and layout of the App
Back End
FastAPI (Python)
ctypes (DLL/.so)
Keyence LJ-X8400 SDK – sensor communication
Front End
React.js
@react-three/fiber & @react-three/drei visualizationChart.js
CSS – for styling
WebSocket / Fetch API
Sensor/
Controller
Ethernet
REST API
Web Socket
Muhammad Zeeshan Yousaf

## Slide 6: About L J-X8400
Laser
  Blue semiconductor laser having 10 mW output.
Data
  3,200 data points per profile.
Range
  In X- direction up to 240 mm ( at 0 Level)
  In Z direction from 380 mm
Interface
  Ethernet TCP
  USB
Measurement Principle
  Laser Triangulation
Muhammad Zeeshan Yousaf

## Slide 7: Controller Functionalities
Ip Setting
Ethernet communication
Encoder and input controls
Sample rate setting
Dead zone Interpolation
Filter Setting
Laser Brightness and Intensity
Tilt Correction
Muhammad Zeeshan Yousaf

## Slide 8: Data Flow in App
Sensor
Back END
Front END
Compare Data
2D Data
3D Data
Live Data
Data Packet
Height Points
Plot x axis / z axis
Data stored on local storage
CSV
Data From local storage
Muhammad Zeeshan Yousaf

## Slide 9: Data Cleaning / Dead zone Removal
Muhammad Zeeshan Yousaf

## Slide 10: Detailed Explanation
Back End
Front End
2D Data + Compare Data
3D Data
Muhammad Zeeshan Yousaf

## Slide 11: What is a Server & Why We Need It Here
A server is an application that listens for requests from clients (frontend/UI) and sends back responses (data or actions).
In our application, the backend server:
• Acts as a bridge between the React UI and the Keyence LJ-X8400 sensor
• Handles requests like connect, disconnect, get profile
• Ensures controlled, secure communication with the sensor hardware
Without a server:
• The frontend would have to connect to the sensor directly, which is not feasible due to protocol complexity and security constraints.
Kasmin Talukdar

## Slide 12: Why We Use FastAPI (vs Django / Node.js)
Fast API Advantages:
• High performance
• Easy to write clean, modern Python code
• Built-in async support for non-blocking calls to the sensor
Why not Django:
• Django is heavier, better for full web apps with templating, DB, we only need a fast API layer
Why not Node.js:
• Would require rewriting all sensor handling logic in JS
• We already use Python for the Keyence SDK wrapper and data processing
Kasmin Talukdar

## Slide 13: High-Level Backend Architecture
Frontend (React) → HTTP API calls → Backend (FastAPI) → Sensor Logic (sensor.py) → Wrapper (LJXAwrap.py) → Native C library → Controller → Sensor head
Each layer has a specific job — separation makes it easier to debug, maintain, and extend
Kasmin Talukdar

## Slide 14: Frontend to Backend Communication
Frontend calls endpoints: /connect, /status, /profile
CORS middleware allows cross-origin requests from http://localhost:3000
Backend parses request, triggers sensor.py functions, returns JSON
Kasmin Talukdar

## Slide 15: FastAPI Routing
Routes:
• POST /set_sensor – store IP & port in state
• POST /connect – connect to sensor
• POST /disconnect – disconnect
• GET /status – connection state
• GET /profile – latest profile data
GET = retrieve without changing state
POST = actions that change backend state
Kasmin Talukdar

## Slide 16: Backend to Sensor Layer
Controller = The hardware control unit between PC and sensor head
LJX8IF_EthernetOpen opens TCP/IP session to controller
Backend sends/receives binary data via Keyence SDK functions
CORS not involved here (only UI ↔ backend)
Ashwini Joshi

## Slide 17: Data Streaming Concept
Maintain open connection → continuously read sensor profiles without reconnecting every time
Backend streams latest data upon frontend request
Benefits: low latency, real-time updates
Ashwini Joshi

## Slide 18: Middleware & Python Wrapper
Middleware & Python Wrapper
Middleware: CORS layer in FastAPI — lets browser frontend call backend despite different origin
Python wrapper: LJXAwrap.py bridges Python and the native LJX8_IF.dll / .so library
Without wrapper: Python can’t directly call C API functions from Keyence SDK
Ashwini Joshi

## Slide 19: Sensor Range Handling (Why)
Raw Z from Keyence can be negative depending on calibration/reference
We shift Z to always be ≥ 0 for clear visualization
Code adds +43 mm offset after conversion from raw units
Ashwini Joshi

## Slide 20: Sensor Range Handling
Strategies:
• Fixed offset (+43 mm) — simple and stable
• Auto-baseline — shift so min(Z) is zero each time
• Use controller’s ZUnit for accurate scaling
Ashwini Joshi

## Slide 21: Frontend Architecture Overview
React.js + TailwindCSS for modern UI development
Component-based architecture with reusable modules
React Router for navigation between different data views
Context API for global state management
Real-time data visualization with SVG charts
Utkarsh Mishra

## Slide 22: Application Structure & Routing
4 main pages: Live Data, 3D Data, Captured Data, Compare Data
Sidebar navigation with collapsible design
Header with application title and controls
Help center modal for user guidance
Responsive design for different screen sizes
Utkarsh Mishra

## Slide 23: Live Data Page & Real-time Capture
Real-time laser profile visualization
Start/Stop/Pause capture controls
Settings modal for sensor configuration
Data export to CSV format
Zoom and pan controls for detailed analysis
Utkarsh Mishra

## Slide 24: Data Flow Process
User opens Live Data page
Frontend checks sensor status via /status endpoint
User configures sensor settings and clicks Connect
Backend establishes connection to physical sensor
User clicks "Start Capture" to begin data collection
Frontend polls /profile endpoint every 200ms
Real-time data is visualized as SVG line charts
User clicks "Stop Capture" to end collection
Data is automatically exported as CSV file
Captured data can be viewed in other pages for analysis
Utkarsh Mishra

## Slide 25: Data Management & Context System
ScanDataContext for global state management
Persistent storage using localStorage
Multiple data collections: live, captured, 3D, compare
Measurement tools with distance calculations
Data sharing between components
Utkarsh Mishra

## Slide 26: Backend Integration & Data Flow
FastAPI backend with CORS enabled for localhost:3000
RESTful API endpoints: /status, /connect, /disconnect, /profile, /set_sensor
Real-time polling mechanism for live data
Error handling and connection status indicators
Sensor control through Python wrapper
Utkarsh Mishra

## Slide 27: 2D Capture Data Page
View one stored scan
Load CSV → show “Scan i / N”
Slider jumps between scans
Measure On toggles rulers/point-pick
Wheel = zoom, drag = pan
Muhammad Hasan Khan

## Slide 28: 2D Capture Page flow
Load CSV
Move slider to a scan
Turn Measure On
Drag A/B markers
Read ΔX, ΔZ, straight distance, angle
Muhammad Hasan Khan

## Slide 29: CSV loading
User selects CSV, read as plain text
Split lines; each row is one scan
Rebuild data if X missing
Update UI: “Scan 1/N”, enable slider and measuring
Compare page repeats this for Left and Right
Muhammad Hasan Khan

## Slide 30: Measuring (what it computes)
Z@A, Z@B via linear interpolation
ΔX = |xB − xA|
ΔZ = |zB − zA|
Straight distance
Angle
Path distance
GO TO APPLICATION
Muhammad Hasan Khan

## Slide 31: Compare 2D Data
Two panels: Left and Right
Each has its own Load, Measure, Slider
Use to compare shape/values side-by-side
Muhammad Hasan Khan

## Slide 32: Compare Data Page flow
Compare page: load left CSV and right CSV
Compare page: enable Lock Compare
Compare page: scrub slider to view matched scans
Compare page: disable Lock to move independently
Compare page: use Point Measure to compare a feature
Muhammad Hasan Khan

## Slide 33: Measuring (what it computes)
Z@A, Z@B via linear interpolation
ΔX = |xB − xA|
ΔZ = |zB − zA|
Straight distance
Angle
Path distance
Muhammad Hasan Khan

## Slide 34: Lock Compare (how it works)
locked = one slider drives both
On left change → right Current = leftCurrent
Unlock to move independently
GO TO APPLICATION
Muhammad Hasan Khan

## Slide 35: Saving/ using CSV
Live capture collects scans in memory
Save builds a CSV: header, then one row per scan
Each row = comma-separated sample values (x optional, z required)
File downloads as .csv for reuse
2D and Compare pages load this same format
Compare loads one file per side; Lock Compare works
best when scan counts match
Muhammad Hasan Khan

## Slide 36: Components Main Functionalities
Profile Viewer
Renders the profile curve
handles zoom, pan, rulers, and point-pick
Scan Data Context
Holds left and right scans for Compare
Implements Lock Compare by syncing right and left when locked is true, and scans for 2D page
Muhammad Hasan Khan

## Slide 37: 3D Layout
3D Stitching- Viewer3D
The 3D surface is made by stacking 2D profile next to each other.
Triangles are built between adjacent height points to form a surface.
3D surface created using mesh principle.
Amritha Anitha Vasanthan

## Slide 38: 3D Layout
3D page (to app)
Amritha Anitha Vasanthan

## Slide 39: 3D viewer- buttons
Left side- 3D surface view, right side-2D slice and measurement panel.
Load new data button- Loads new scanned surface data, CSV file.
X/Y Slice- To chose slice direction.
Show hide slice- Toggle slice panel visibility.
Slice slider- To move plane across the object to select profile.
Reset
Zoom in/out
clear
Amritha Anitha Vasanthan

## Slide 40: Extract slice from 3D
Click on the ‘show slice’
Slider to desired location
Selected profile automatically appears in the 2D viewer.
Amritha Anitha Vasanthan

## Slide 41: 2D slice and measurement panel
Amritha Anitha Vasanthan

## Slide 42: Measurement modes
Measure on Path distance
Point measure for straight distance, path distance, angle.
Amritha Anitha Vasanthan

## Slide 43: Applications
Industrial Automation
Smart packaging
Quality control
Industrial inspection and maintenance
Integration on robots
Amritha Anitha Vasanthan

## Slide 44: Future Work
Automated conveyor system for Consistent Scanning.
Adaptive Filtering based on Measurement Parameters.
AI/ML based Damage Classification.
AI Assisted Correction and Measurements.
Amritha Anitha Vasanthan

## Slide 45
THANK YOU
QUESTION?
Amritha Anitha Vasanthan